| This is a TEMPLATE (Please describe your means & methods for installing flooring material) Floor Prep and Layout: Example: Demo and Float floor with silica base product. (See chemical JHA) Install Carpet/Vinyl/VCT & Base: Example: Apply adhesive Install Carpet/Vinyl/VCT_____ sf 4’-6” cove base _____________lf House Keeping & Clean-Up: | Risks of injury from improper lifting | All employees shall be instructed in safe lifting techniques. If loads are awkward, too heavy, high traffic areas, two (2) men are required for carrying loads 10’ or greater. |
| --- | --- | --- |
|  | Risk of exposure to asbestos from VCT/ Mastic under lament | When laying carpet over a VCT floor, “Do Not Disturb” existing tile while prepping. If a tile becomes loose, broken or missing “Stop” work and notify the C/M-P/M immediately. |
|  | Risk of exposure to silica based products | Respirators maybe need to mix Silica based products. Respirator Program with medical eval & fit test may also be required. (check with EH&S IH) |
|  | Risk of fire from heat gun or open flamed tool | Follow the Hot Work permit as required. Fire watch is required (trained in fire extinguishers). Employee shall have proper training on heat guns or open flamed tools. |
|  | Risk of injuries/ cuts from improper tool use or storage. | Employees are to be trained on the use of tools. Protect knifes or open blade with a holder or sheath to protect the blade while not in use. Keep all used razor blades in a sharps container labeled as "SHARPS |
|  | Risk of injuries due to Slips, Trips & Falls | Housekeeping shall be maintained but not limited to hourly/daily, as site conditions change or as needed. |

| Employee Signatures: | Date: |  | Employee Signatures: | Date: |  | Employee Signatures: | Date: |
| --- | --- | --- | --- | --- | --- | --- | --- |

A signed copy of this JHA must be posted while the applicable subcontractor is working on-site and be available to any LBNL employee upon request.